# Purpose
To provide instructions for the product level assembly of PN 10000001 (ASSY,AIRCRAFT WIRELESS).
# Scope
This work instruction shall be used for internal use only, it is suitable for providing to 3rd-party contract assemblers.
## Definitions
None.
## Records Retention
A record of the serial number and the manufacturing test results must be entered in Maestro.
# Responsibility and Authority
The Director, Manufacturing, has responsibility and authority for maintaining this work instruction. The assembler is responsible for correct assembly of devices according to this work instruction.
# Procedure
## Health and Safety Concerns
Safety glasses and shoes are recommended.
## Required Equipment
Screwdrivers	#2 Philips screwdriver medium flat-blade screwdriver
Product serial number label	Standard 3x5-inch label containing PN, Name, and S/N printed from Maestro.

## Assemble Product
1. Print a BOM (bill of materials) using Maestro and pick the necessary parts.
2. Assemble the enclosure according to the assembly drawing.
3. Re-test the assembled enclosure using the PCA test procedure (see 20000003_WI).
  Note: connect the antenna to the Yellow binding post.
  1. If the test passes, log into Maestro, print a serial number product label and affix the serial number label to the enclosure.
  2. If the test does not pass, repair the unit and repeat the test.
# Related and Support Documentation
None.
# Revision History
Date	Name	Change Description
2013-01-01	Hank Baldwin	Creation
2013-01-03	Hank Baldwin	Revised for Product Release